2014 Regulations

Introduction

The following technical regs are set out in accordance with the MSA format and it should be clearly understood that unless it says clearly that you CAN DO IT, you should work on the principle you CANNOT.

No modifications mechanically or physically to the car as sold by Honda, unless otherwise stated within these regulations.

IF YOU ARE UNSURE OR YOUR CARS ELIGIBILITY TO THE SERIES PLEASE FORWARD A SPEC SHEET TO……………………. Shaun@Civic-Cup.co.uk

Whilst every effort has been made to ensure the information is accurate it is the driver’s responsibility to ensure his/her car meets Blue Book regulations in all matters.

Where parts are replaced they should be with Honda manufactured components from the manufacturer’s parts list for the model being raced.

In the interest of cost non generic Honda replacement parts can be used, where they can be shown and proven to be of the same material, manufacturing process, form, shape, function and fit without modification as the original.

1.0 	Entrants Requirements

1.1 	Entrants must be in possession of a valid current MSA Entrants Licence where applicable and be members of the Civic Racing Club LTD.

1.2 	Drivers and Entrant/Drivers must  be  fully  paid  up  valid members of the Civic Racing Club and be registered for the Series and be in possession of a valid MSA Competition (Racing) minimum National B Status Licence.

1.3	All necessary documentation must be presented for checking at all the rounds when signing-on.

The organisers reserve the right to invite Guest Competitors to take part in any round or number of rounds, however these competitors will not receive any Series Trophy’s but may be eligible for Driver of the Race award.. Any competitor wishing to compete for a single race may do so, but cannot claim Podium Positions unless registered for the series for the full 2013 season.

2.0	 Description

2.1 	The Civic Racing Club -Civic Cup series is for all Honda Civics with B16 Engines

2.2 	All models being raced must strictly abide by the Maximum BHP Limit and Minimum Weight.

2.3 	If the Entrant is found to be over the BHP Limit, or under the weight limit, Ballast will be added to compensate

2.4 	All cars must comply with (though do not need) MOT requirements (excluding emissions), be of sound construction and mechanical condition and well maintained.

2.5	There is no need for an MOT certificate, road tax or insurance unless driven to the circuits.

3.0 	Qualification

3.1	Each driver should complete a minimum of 3 laps practice in the car to be raced and in the correct session in order to qualify for selection and order of precedence as set out in the MSA regulations Q4.5 The Clerk of the Course and/or Stewards of the Meeting shall have the right to exclude any driver whose practice times or driving are considered to be unsatisfactory as per MSA Regulation

3.2	The grid for race 1 will be decided by the fastest times in qualifying . The grid for race 2 will be the finishing order of race 1.  Non finishers and competitors not classified in the race results will be placed on the back of the grid in order of distance covered. In the event of a tie the order will be at the discretion of the Clerk of Course. At some events the club reserves the right to reverse the grid on the final race of the day, i.e. winner of race one will start in last position, 2nd place will start 2nd to last etc. This may be reduced to the top 8 depending on the number of competitors. The format will be confirmed in the 2013 calendar.

4.0 	Races

4.1	The standard minimum scheduled time shall be min 20 minutes whenever practicable but should any race distance be reduced at the discretion of the Clerk of the Course or Stewards of the Meeting it shall still count as a full scoring round

    - Safety

5.1 	Drivers should ensure that both they and their cars conform in every way with the MSA Blue Book, with specific regard to safety matters. You are particularly drawn to, though not exclusively, the installation of roll cage, race seat, harness, fire extinguisher, and you’re racing clothing.

6.0 	Chassis

6.1 	CLUB CONTROLLED PARTS ONLY No modifications to original chassis and chassis pick points allowed.

7.0 	Car Exterior

7.1 	No alterations to the shape of standard bodywork. The basic car must retain its original silhouette.

7.2 	Wing mirrors must be retained but may be replaced with aftermarket type, wiper blades must function, and all lights must function.

7.3	Towing eyes must be painted in accordance with the MSA regulations.

7.4	No modifications may be made to the body work other than repairs, although single skinning panels to reduce weight is allowed.

7.5	Exterior trim should remain standard, aftermarket bumper lips and rear spoiler may be fitted. (club approved Products)

7.6	No widening of the wheel arches is permitted.

7.7	Bonnet and engine covers to be in normal closed position with no non standard gaps. No use of tape to fill shut lines.

7.8	Front screen to be of laminated type and as per MSA rules. Club approved Lexan window kits may be used.

8.0 	Interior

8.1	Drivers seat may be replaced and there is no passenger seat requirement.

8.2	Floor coverings and roof linings may be removed.

8.3	A dash must remain in situ, but radio, stereo units, speakers, heater system and associated ducting/wiring as well as the spare wheel and tools may be removed.

8.4	Steering wheel can be replaced.

8.5	Glass sunroofs must be removed and the opening enclosed in accordance with MSA regulations.

8.6	Electric window motors and door cards can be removed but the doors must be covered in accordance with MSA regulations.

8.7	All cars must be fitted with an MSA approved roll cage.

9.0 Ground Clearance

9.1	It is permitted to alter the ride height but the car must be no less than 75mm from the ground in race trim with driver stationary.

10.0 Engine

10.1	Honda B16 Engines only with no more than 190bhp at the flywheel, and only normally aspirated.

10.2	The engines are to be run in standard specification with standard components.

10.3	No internal performance enhancing modifications to the engine are permitted. Incl , cams, pulleys, valves, pistons, con rods etc.

10.4	All engines will be checked for compliance

10.5	Cars may be a onsite Dyno for testing and checking compliance.

10.6	All components must be as per Honda factory, Pattern parts allowed to OEM spec. The use of standard or standard pattern parts and components only to be used for rebuilds which should be within the tolerances set down by Honda’s workshop manuals.

10.7	The Performance of cars may be checked by means of an advanced motorsport GPS logger at each meeting.

10.8	Any engine found to have increased power of more than 2% will have ballast added to compensate.

10.9	If power is found to be substantially over the 190bhp limit the car will be refused entry.

10.10 	Any engines that are rebuilt after being tested, may be re-tested as above. All cost’s for above to be borne by the entrant.

10.11      All Engines and ECUs must be sealed at club approved Dyno centre prior to start of the season.

11.0 	Oil and Water Cooling

11.1	Replacement alloy radiator can be used. (Club Controlled Only)

11.2	Standard sump to be retained, but may be baffled.

11.3	Oil coolers may be fitted.

12.0 	Induction System

12.1	After market cold air intakes and air filters are allowed and can be fed with direct air feed. (Club controlled item only)

    - No Forced Induction of any kind

12.3 	Induction system is from the throttle body NOT FROM THE CYLINDER HEAD

- Exhaust System

13.1       Manifold and system may be changed to a club approved product only.

- Ignition System

  - Standard ECU only to be used (no remapping). Spark plugs and HT leads free.

  - ECU must be sealed at Club approved dyno centre

15.0 	Fuel System

15.1	Fuel pump, fuel rails, and injectors to remain standard, fuel lines and filter are free.

  - Fuel Tank may be baffled or swirl pots fitted.

  - There must be a minimum of 2.5ltrs left in the tank after each race for sampling reasons.

16.0	Suspension

16.1	Club Controlled only shocks and springs are allowed, providing they mount on the standard mounts. Must be Club Approved Product.  MUST BE MONO TYPE

16.2	Anti-roll bars are free, but must not be adjustable by the driver when seated.

16.3	Poly bushing replacements are permitted. (Super Pro)

16.4	Modifications to suspension pick up points, cockpit adjustable anti roll bars whilst driver is seated, offset or adjustable suspension strut mounts or hub carrier brackets, dampers with remote reservoirs are Prohibited

17.0 Wheelbase and Track

17.1	Wheelbase and track to remain standard for the model being raced.

17.2        tyre size, 205/50/15 or 195/50/15

18.0 	Transmission

18.1	Must remain as H Pattern gearbox with Syncro Engagement only.

No Dog Engagement Type or sequential type boxes

18.2        Any Honda B series Gearbox may be used, Final Drive ratios may be changed from stock

18.3	Carbon coated syncros may be used, ( club approved supplier)

18.4	A controlled limited slip differential or torque biasing differentials may be used. (club control part only)

18.5	Up-rated clutch may be used. (club control part only)

19.0 Electrics

19.1	Ignition system standard, spark plugs and HT leads free.

19.2	All lights to remain operative as per MOT standards.

19.3	Rain light must be present in accordance with Blue Book regulations.

19.4	Batteries may be repositioned, no external slave batteries to be used.

19.5	Car must be capable of repetitive starts of main/only battery.

19.6	A fully working and standard alternator and pulley must be fitted.

19.7	Engine cut of switch fitted in accordance with Blue Book.

19.8	The cars key starting mechanism can be replaced with a push button starter.

19.9	Cut off switch must be fitted as per Blue Book.

20.0	Brakes

20.1	Discs & Callipers must be of standard type, pattern, HONDA OEM PARTS ONLY.

20.2	Brake Pads & Discs must be OEM SIZES

20.3	MAXIMUM SIZE PERMITTED 282mm, HONDA OEM PARTS ONLY

20.4	Brake Bias may be fitted

21.0	Wheels and Steering

21.1	Wheels must be standard size for the model being raced.(see 21.3)

21.2	Steering locks to be rendered inoperative unless cars are driven to the circuit, in accordance with Blue Book J20.6.

21.3	Wheels must be 15x7 or 15x6/6.5

22.0	Tyres

22.1	The control tyre is the TOYO R888 GG Compound, tyre size options, 205/50/15 or 195/50/15

22.2 	These tyres are mandatory to be eligible to run in the series and will be marked CC.

22.3	No alteration to the tyres from the manufacturers specification is permitted.

22.4	No heat retention devices or tyre treatments allowed.

22.5	No re-cutting, re-grooving or any way that modifies the tread pattern is allowed.

22.6	All manufacturer’s data should be clearly visible.

22.7      	All Tyres MUST be purchase from   Mike Stokes MotorSport  TEL. 01202 547555/548000

info@mikestokes.net  and will be marked for use in the Civic Cup 2013. Entrants must provide race number and Club membership number to obtain club rates.

23.0 Vehicle Weights and Power

23.1	It is the responsibility of the entrant to ensure that the driver and car combination meet the minimum requirements.

23.2	The minimum weight of the driver and car combination including post race fuel is 1025kg.

23.3	The top 5 driver and car combinations will be weighed after qualification and race for compliance with regulation, other cars will also be weighed at the discretion of the club after each session.

23.4	Alternate Materials may be used in order to meet the Weight Limits.

23.5	Added weight must be as per blue book regulation and subject to approval of even scrutineer

23.5	Cars found to be under the weight will be subject to a penalty and the entrant must ensure that the driver/car combination complies with clause 23.1 above.

24.0	Fuel Tank and Fuel

24.1	Tanks must be standard in type and position and incorporate a non return valve in vent system.

24.2	Fuel allowed as per MSA regulations.

24.3	No Race Fuels over 99Ron

25.0	Silencing

25.1	All vehicles must comply with current MSA regulations. 105DB Max

26.0	Driver Aids

26.1	Driver aids such as data loggers or shift lights can be used during race meetings subject to fitment acceptability by scrutineers.

27.0	Series Sponsorship

27.1	All vehicles must carry any series sponsor decals as per club approved pattern.

27.2	Car livery and personnel sponsors are free, but must have club approval prior to racing.

27.3	MSA Regulation J 4.1 applies. Numbers must be clearly displayed on either side of the car and on the screen in a position acceptable to the Timekeepers.   .

27.4

1. Positions: The race numbers for each rear side window shall be;

(i) A minimum of 200mm high

(ii) With a stroke width of at least 20mm

(iii) Colored Day-Glo yellow.

In addition, the windscreen of all cars must display the competition

number positioned on the upper area of the passenger’s side of the

windscreen, as follows;

(i) The numerals must be at least 150mm high

(ii) Be in the same color and font as those displayed on the rear side

windows

(iii) Be placed no closer than 50mm from the lower edge of the

windscreen “sun-strip” and 50mm from the side edge of the

windscreen.

750 Motor Club decals must be affixed prominently. Series

Sponsor’s decals (where applicable) must be affixed in or near the

positions detailed on the diagram supplied with those decals. 750

Motor Club and Championship Sponsor’s decals must take preference

to any other decals. Drivers may be requested to remove decals that

are viewed as conflicting with official Series Sponsors. Failure

to comply will render the vehicle and driver ineligible to race.

28.0	Parts Supply

28.1

28.2	Tyres Must be purchased Direct from the designated club supplier as Cl 22.7

28.3 	Club will issue approved parts list for purchase through the club or series sponsors.

29.0 	Penalties for non compliance of the Regulation 23

29.1 	Following a qualification or race session any Driver and car combinations found to be less than 5kgs under the weight  limit as set out in cl 23.2 will be relegated 5 grid positions.

29.2 	Following a qualification or race session and driver and car combination found to be more than 5kgs under the weight  limit as set out in cl 23.3 will be relegated to the rear of the grid.

29.3	In the event that there are more than one car found to be under the weight limit the lightest car and driver combination will be positioned in last place with the next lightest taking up the next grid position in front and so on.

30.0	Code of Conduct

30.1	The Series is run by the The Civic Cup and will appoint a Representative to be the point of contact for the entrants.

30.2	The Entrants shall appoint from within the group a suitable person or persons (max2) to represent the drivers/entrants.

30.3	In the event that a driver or entrant has had cause to be disciplined by the clerk of the course during an event for causing a collision,  poor driving standards and/or un sportsmanlike behavior on or off the circuit, either from the entrant, driver or support members, the Club will reserve the right to consider the incident and if it feels that the integrity and cordiality of the series has or may be adversely affected the ‘Club’ may refuse  any further participation in the event, and ask that the entrant to leave the venue and may refuse any further entries.

30.4	In the event that an entrant or driver who has been asked to take no further part in the race series as outlined in 30.3 above, any entry fees paid in advance will be forfeited, as the club will have made a financial commitment to the event organisers based on the initial entries at the start of the race season.

30.5	If following an event a driver considers that he has reason to complain about poor driving standards that has not been reported to the CofC, he shall bring the matter to the attention of the drivers representatives, who will seek further substantiation from other drivers and shall take the matter to the Club representative for disciplinary action.

30.6      ALL Cars must run in car camera and footage must be made available to club representative upon request.